## Slide 1
WHK Documentation
Yanxia Lu
Chair of Radio Frequency and Photonics Engineering

## Slide 2: Outline

## Slide 3: Main Tasks
Mathematical modeling of active silicon micro ring resonators (MRRs) with feedback control considering various nonlinear optical effects. Mathematische Modellierung aktiver Silizium-Mikroringresonatoren (MRRs) mit Rückkopplungssteuerung unter Berücksichtigung verschiedener nichtlinearer optischer Effekte.
Numerical simulation of the time and frequency response of the MRRs with feedback control using Python & MATLAB. Numerische Simulation des Zeit- und Frequenzverhaltens der MRRs mit Feedback-Steuerung unter Verwendung von Python & MATLAB.

## Slide 4: Week 1
Theory Background
  Ising Model and Ising Machine
    https://nbviewer.org/url/jakevdp.github.io/downloads/notebooks/CythonIsingModel.ipynb
    https://matthewrocklin.com/blog/work/2015/02/28/Ising
  Pitchfork Bifurcation
    https://www.youtube.com/watch?v=Il75BOO94jY&t=2134s
Quench of an Ising system on a two-dimensional square lattice (500 × 500) with inverse temperature β = 10, starting from a random configuration.
https://en.wikipedia.org/wiki/Ising_model
Ising Model
https://social-innovation.hitachi/en-us/case_studies/new-computer-can-quickly-solve-combinatorial-optimization-problems/
McCann, Caitlin. "Bifurcation Analysis of Non-linear Differential Equations." The University of Liverpool (2013).

## Slide 5
Literature Review
  Realization of optical bistability through nonlinear optical resonator:
    Ising Machines: Non-Von Neumann Computing with Nonlinear Optics - Alireza Marandi - 6/7/2019 (https://www.youtube.com/watch?v=V7BxJsLyubk&t=832s)
    “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” (2020) Appendix A.
    “A Review of Simulation Algorithms of Classical Ising Machines for Combinatorial Optimization” (2022)
    “Ising Machines: Hardware Solvers for Combinatorial Optimization Problems” (2022)

## Slide 6: Simulation
Read through “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” (2020) Appendix A.
Plotted the characteristic function from Appendix A

## Slide 7: Week 2-3
Investigated an existing ising machine simulation algorithm to understand the numerical modelling of CIM, in order to prepare fundamental knowledge for future construction of quantitative model of ising machine with performance relevant parameters.
  classical models of the CIM
    CIMs with “error correction.”: chaotic amplitude control (CAC), amplitude-heterogeneity correction (AHC), and amplitude-heterogeneity correction with external field terms (AHC). The first two solvers do not have an external field, while the latter requires an external field ℎ.
Chen, F., Isakov, B., King, T., Leleu, T., McMahon, P., & Onodera, T. (2022). cim-optimizer: a simulator of the Coherent Ising Machine [Computer software].
https://github.com/mcmahon-lab/cim-optimizer
https://cim-optimizer.readthedocs.io/en/latest/problem_description.html

## Slide 8
Locally installed the module and tried out different parameters to understand the model with Example 1: MAX-CUT with the CIM.

## Slide 9
Found further possible model to investigate：
  Monte Carlo simulation of the Ising model:
  https://github.com/jfaraudo/Ising-model
  Simulation of the experiment from paper:
  Böhm, F., Verschaffelt, G. & Van der Sande, G. A poor man’s coherent Ising machine based on opto-electronic feedback systems for solving optimization problems. Nat Commun 10, 3538 (2019). https://doi.org/10.1038/s41467-019-11484-3
  https://github.com/gautham-umasankar/Ising_model/tree/master

## Slide 10: Week 4
Re-read Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators - Appendix A
  To understand the pumping threshold to have multi-stability in a single nonlinear resonator
  To understand single mode ordinary differential equation
  Validated the relationship in Fig. 2 by plotting

## Slide 11: Week 5
Read through “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” - Appendix B
  To understand the open-loop and closed-loop model with two ring resonators
Tezak, Nikolas, et al. "Integrated coherent Ising machines based on self-phase modulation in microring resonators." IEEE Journal of Selected Topics in Quantum Electronics 26.1 (2019): 1-15.

## Slide 12: Week 6-9
Read over and over again “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” - Appendix B
  Tried to plot Fig. 11 but faied to understand the meaning of x-axis in Fig.11. Read more about pitchfork bifurcation, especially about the stabilizing influence of higher-order terms in subcritical case.
Strogatz, S.H. (2015). Nonlinear Dynamics and Chaos: With Applications to Physics, Biology, Chemistry, and Engineering (2nd ed.). CRC Press.
https://doi.org/10.1201/9780429492563

## Slide 13
Had difficulty to plot exact the same graph and realized that I didn‘t fully understand how the tunable amplifier could achieve ideal symmetrically bistable spin in the subcritical working region.
  As shown below, the left one is my plot, and the right one is Fig. 4 (right) from the paper "Integrated coherent Ising machines based on self-phase modulation in microring resonators."
Tezak, Nikolas, et al. "Integrated coherent Ising machines based on self-phase modulation in microring resonators." IEEE Journal of Selected Topics in Quantum Electronics 26.1 (2019): 1-15.

## Slide 14: Week 10
Went back to literature to understand how CIM works
  With sub-harmonic injection locking (SHIL), bistable states have a phase difference of 180° almost any nonlinear self-sustaining oscillators can be applied to realize Ising machine, with logic values encoded in their phases [1].
  https://www.spiedigitallibrary.org/conference-proceedings-of-spie/11703/117030D/Integrated-coherent-Ising-machines-for-next-generation-optimization-accelerators/10.1117/12.2585839.full
  Mapping of NP-hard problems to Ising problem, e.g. Max-cut
[1] Wang, Tianshi, and Jaijeet Roychowdhury. "Oscillator-based Ising machine." arXiv preprint arXiv:1709.08102 (2017).

## Slide 15: Max-cut
The MAX-CUT problem on an undirected graph G = (V, E) with an edge weight function w : E → R is one of them, where V and E denote the sets of vertices and edges respectively. The goal of the MAX-CUT problem is to find a cut (S, V \ S) such that the sum of the weight of the edges with one endpoint in S and the other in V \ S is maximized over all possible cuts [8]. Let wjl = wlj be the edge weight if (j, l) ∈ E and wjl = 0 if (j, l) ∈/ E, and σj = +1 if the j-th vertex is in S and σj = −1 if not. The weight of a cut S is thus given by
Wjl-Jjl, max-cut corresponds to the ground state of Ising problem.
Wang, Zhe, et al. "Coherent Ising machine based on degenerate optical parametric oscillators." Physical Review A 88.6 (2013): 063853.

## Slide 16: Week 11
Wrap up the first phase
  Tried to understand linearity near threshold and the corresponding linear gain in “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” [1], along with the paper from the same author “A coherent perceptron for all-optical learning” [2].
  Validated the linear transferfunction by plotting Fig.4 in [1] (left). Code available on https://github.com/AllInCoffee/Playground/tree/main
[1] Tezak, Nikolas, et al. "Integrated coherent Ising machines based on self-phase modulation in microring resonators." IEEE Journal of Selected Topics in Quantum Electronics 26.1 (2019): 1-15.
[2] Tezak, N., Mabuchi, H. A coherent perceptron for all-optical learning. EPJ Quantum Technol. 2, 10 (2015). https://doi.org/10.1140/epjqt/s40507-015-0023-3

## Slide 17: Week 12