## Slide 1
WHK Documentation
Yanxia Lu
Chair of Radio Frequency and Photonics Engineering

## Slide 2: Outline

## Slide 3: Main Tasks
Mathematical modeling of active silicon micro ring resonators (MRRs) with feedback control considering various nonlinear optical effects. Mathematische Modellierung aktiver Silizium-Mikroringresonatoren (MRRs) mit Rückkopplungssteuerung unter Berücksichtigung verschiedener nichtlinearer optischer Effekte.
Numerical simulation of the time and frequency response of the MRRs with feedback control using Python & MATLAB. Numerische Simulation des Zeit- und Frequenzverhaltens der MRRs mit Feedback-Steuerung unter Verwendung von Python & MATLAB.

## Slide 4: Week 1
Theory Background
  Ising Model and Ising Machine
    https://nbviewer.org/url/jakevdp.github.io/downloads/notebooks/CythonIsingModel.ipynb
    https://matthewrocklin.com/blog/work/2015/02/28/Ising
  Pitchfork Bifurcation
    https://www.youtube.com/watch?v=Il75BOO94jY&t=2134s
Quench of an Ising system on a two-dimensional square lattice (500 × 500) with inverse temperature β = 10, starting from a random configuration.
https://en.wikipedia.org/wiki/Ising_model
Ising Model
https://social-innovation.hitachi/en-us/case_studies/new-computer-can-quickly-solve-combinatorial-optimization-problems/
McCann, Caitlin. "Bifurcation Analysis of Non-linear Differential Equations." The University of Liverpool (2013).

## Slide 5
Literature Review
  Realization of optical bistability through nonlinear optical resonator:
    Ising Machines: Non-Von Neumann Computing with Nonlinear Optics - Alireza Marandi - 6/7/2019 (https://www.youtube.com/watch?v=V7BxJsLyubk&t=832s)
    “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” (2020) Appendix A.
    “A Review of Simulation Algorithms of Classical Ising Machines for Combinatorial Optimization” (2022)
    “Ising Machines: Hardware Solvers for Combinatorial Optimization Problems” (2022)

## Slide 6: Simulation
Read through “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” (2020) Appendix A.
Plotted the characteristic function from Appendix A

## Slide 7: Week 2-3
Investigated an existing ising machine simulation algorithm to understand the numerical modelling of CIM, in order to prepare fundamental knowledge for future construction of quantitative model of ising machine with performance relevant parameters.
  classical models of the CIM
    CIMs with “error correction.”: chaotic amplitude control (CAC), amplitude-heterogeneity correction (AHC), and amplitude-heterogeneity correction with external field terms (AHC). The first two solvers do not have an external field, while the latter requires an external field ℎ.
Chen, F., Isakov, B., King, T., Leleu, T., McMahon, P., & Onodera, T. (2022). cim-optimizer: a simulator of the Coherent Ising Machine [Computer software].
https://github.com/mcmahon-lab/cim-optimizer
https://cim-optimizer.readthedocs.io/en/latest/problem_description.html

## Slide 8
Locally installed the module and tried out different parameters to understand the model with Example 1: MAX-CUT with the CIM.

## Slide 9
Found further possible model to investigate：
  Monte Carlo simulation of the Ising model:
  https://github.com/jfaraudo/Ising-model
  Simulation of the experiment from paper:
  Böhm, F., Verschaffelt, G. & Van der Sande, G. A poor man’s coherent Ising machine based on opto-electronic feedback systems for solving optimization problems. Nat Commun 10, 3538 (2019). https://doi.org/10.1038/s41467-019-11484-3
  https://github.com/gautham-umasankar/Ising_model/tree/master

## Slide 10: Week 4
Re-read Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators - Appendix A
  To understand the pumping threshold to have multi-stability in a single nonlinear resonator
  To understand single mode ordinary differential equation
  Validated the relationship in Fig. 2 by plotting

## Slide 11: Week 5
Read through “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” - Appendix B
  To understand the open-loop and closed-loop model with two ring resonators
Tezak, Nikolas, et al. "Integrated coherent Ising machines based on self-phase modulation in microring resonators." IEEE Journal of Selected Topics in Quantum Electronics 26.1 (2019): 1-15.

## Slide 12: Week 6-9
Read over and over again “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” - Appendix B
  Tried to plot Fig. 11 but faied to understand the meaning of x-axis in Fig.11. Read more about pitchfork bifurcation, especially about the stabilizing influence of higher-order terms in subcritical case.
Strogatz, S.H. (2015). Nonlinear Dynamics and Chaos: With Applications to Physics, Biology, Chemistry, and Engineering (2nd ed.). CRC Press.
https://doi.org/10.1201/9780429492563

## Slide 13
Had difficulty to plot exact the same graph and realized that I didn‘t fully understand how the tunable amplifier could achieve ideal symmetrically bistable spin in the subcritical working region.
  As shown below, the left one is my plot, and the right one is Fig. 4 (right) from the paper "Integrated coherent Ising machines based on self-phase modulation in microring resonators."
Tezak, Nikolas, et al. "Integrated coherent Ising machines based on self-phase modulation in microring resonators." IEEE Journal of Selected Topics in Quantum Electronics 26.1 (2019): 1-15.

## Slide 14: Week 10
Went back to literature to understand how CIM works
  With sub-harmonic injection locking (SHIL), bistable states have a phase difference of 180° almost any nonlinear self-sustaining oscillators can be applied to realize Ising machine, with logic values encoded in their phases [1].
  https://www.spiedigitallibrary.org/conference-proceedings-of-spie/11703/117030D/Integrated-coherent-Ising-machines-for-next-generation-optimization-accelerators/10.1117/12.2585839.full
  Mapping of NP-hard problems to Ising problem, e.g. Max-cut
[1] Wang, Tianshi, and Jaijeet Roychowdhury. "Oscillator-based Ising machine." arXiv preprint arXiv:1709.08102 (2017).

## Slide 15: Max-cut
The MAX-CUT problem on an undirected graph G = (V, E) with an edge weight function w : E → R is one of them, where V and E denote the sets of vertices and edges respectively. The goal of the MAX-CUT problem is to find a cut (S, V \ S) such that the sum of the weight of the edges with one endpoint in S and the other in V \ S is maximized over all possible cuts [8]. Let wjl = wlj be the edge weight if (j, l) ∈ E and wjl = 0 if (j, l) ∈/ E, and σj = +1 if the j-th vertex is in S and σj = −1 if not. The weight of a cut S is thus given by
Wjl-Jjl, max-cut corresponds to the ground state of Ising problem.
Wang, Zhe, et al. "Coherent Ising machine based on degenerate optical parametric oscillators." Physical Review A 88.6 (2013): 063853.

## Slide 16: Week 11
Wrap up the first phase
  Tried to understand linearity near threshold and the corresponding linear gain in “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators” [1], along with the paper from the same author “A coherent perceptron for all-optical learning” [2].
  Validated the linear transferfunction by plotting Fig.4 in [1] (left). Code available on https://github.com/AllInCoffee/Playground/tree/main
[1] Tezak, Nikolas, et al. "Integrated coherent Ising machines based on self-phase modulation in microring resonators." IEEE Journal of Selected Topics in Quantum Electronics 26.1 (2019): 1-15.
[2] Tezak, N., Mabuchi, H. A coherent perceptron for all-optical learning. EPJ Quantum Technol. 2, 10 (2015). https://doi.org/10.1140/epjqt/s40507-015-0023-3

## Slide 17: Week 12
Summarize the first phase
Presentation

## Slide 18: Week 13
TSP formulation

## Slide 19: Week 14-15 Literature Review
Literature review on state-of-the-art Kerr Parametric Oscillator (KPO) based Ising machines
  Objectives
    To find a more accurate model for mapping into Ising problems
      Add noise or thermal flucturation (error correction)
      Increase order of nonlinearity in cost function
      Add external magnetic field
    To compute faster
      Optimize the model for less computing complexity
      Reduce bits required for coupling strength
    To be more compact / to scale
      Reduce power consumption
      Reduce footprint

## Slide 20: DOPO Based CIM
Advantage: Scaling
Disadvantage: bulky, amplitude homogeneity  error correction through optimization of model with external magnetic field and addition of noise
NTT Group
Simulating Ising spins in external magnetic fields with a network of degenerate optical parametric oscillators (2020) : model with external field
100,000-spin coherent Ising machine (2021): scaling with time multiplexing
Yamamoto Group
Effect of Coupling Discretization on Coherent-Ising-Machine-Implemented Hopfield Model(2023): reduce the number of bits of coupling strength
Yamamoto, NTT and Standford
Skew-Gaussian model of small-photon-number coherent Ising machines (2024): control of amplitude homogeneity, DOPOs + two third-order fluctuation products

## Slide 21
Yamamoto, NTT and Standford
Mean-field coherent Ising machines with artificial Zeeman terms (2023): implementation of Zeeman terms (external magnetic field) within Mean-Field CIM (MF-CIM) models, improving performance of CIM with chaotic amplitude control in 2022 (Control of amplitude homogeneity in coherent ising machines with artificial zeeman terms (2022)).
Skew-Gaussian model of small-photon-number coherent Ising machines (2024): control of amplitude homogeneity, DOPOs + two third-order fluctuation products
Dynamic Anisotropic Smoothing for Noisy Derivative-Free Optimization (2024) : improve tunning of parameters in CIM with chaotic amplitude control ((Leleu et al., 2019) using DAS (dynamic anisotropic smoothing) algorithm, which is used for derivative-free optimization.

## Slide 22: Opto-electronic Oscillator (OEO) Based Ising Machine
Advantages: fast, low cost, mitigating amplitude inhomogeneity, compact
Disadvantages: periodic transfer function due to the Mach-Zehnder interferometer is an approximation of CIM polynomial model
Applied Physics Research Group, Vrije Universiteit Brussel (VUB)
A poor man’s coherent Ising machine based on opto-electronic feedback systems for solving optimization problems (2019)
Hewlett Packard Labs (HP Labs), Belgium
Tunable coherent Ising machines with fifth-order nonlinearity (2024): a fifth-order nonlinearity to have more hyperparameters and a large noise regime to facilitate exploration
Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators (2019)
VUB + HP Labs
Order-of-magnitude differences in computational performance of analog Ising machines induced by the choice of nonlinearity (2021): higher order helps solve optimization problems
Compact and inexpensive photonic Ising machines based on optoelectronic oscillators (2021): comparison of OEO-based and DOPO-based Ising machines

## Slide 23: Other Integrated Kerr Ising Machines
Columbia University + Cornell University
Demonstration of chip-based coupled degenerate optical parametric oscillators for realizing a nanophotonic spin-glass (2020)
Korea Advanced Institute of Science and Technology, KAIST + Daegu-Gyeongbuk Institute of Science and Technology, DGIST, Korea
Low Power Coherent Ising Machine Based on Mechanical Kerr Nonlinearity (2023)

## Slide 24: Week 16: Free Carrier and Thermal
Literature reading
  On the modeling of thermal and free carrier nonlinearities in silicon-on-insulator microring resonators
  Thermo-Optic multistability and relaxation in silicon microring resonators with lateral diodes - Appendix B
  Conditions for Parametric and Free-Carrier Oscillation in Silicon Ring Cavities - V
  Measurement with Pump and probe technique, modelling with experimental modeling through fitting and finite-element model (FEM)
Refractive index variation due to
→ free carrier dispersion (FCD)  extra loss
→ the temperature variation (thermal-optic (TO))

## Slide 25: The Temporal Dynamics of SOI Microresonator Self-pulsing
The internal energy of MR:
The free carrier population:
The normalized resonance shift induced by ΔT and ΔN:
The rate of int. and ext. loss：
The differential temperature with the cladding ∆T:
When the temperature profile in the surroundings of the MR is
not spatially uniform.
Borghi, M., Bazzanella, D., Mancinelli, M. and Pavesi, L., 2021. On the modeling of thermal and free carrier nonlinearities in silicon-on-insulator microring resonators. Optics Express, 29(3), pp.4363-4377.

## Slide 26
Borghi, M., Bazzanella, D., Mancinelli, M. and Pavesi, L., 2021. On the modeling of thermal and free carrier nonlinearities in silicon-on-insulator microring resonators. Optics Express, 29(3), pp.4363-4377.

## Slide 27: TO Modelling in MR with Lateral PIN Junctions for Active Free Carrier Removal.
The coupling of FC dynamics and thermal optic effect (TOE):
  active free-carrier removal increases TO nonlinearity caused by Joule heating
  Logarithmic time dependence of temperature deflection:
a = 0.155, b = 16 ns and γ ≈ 0.577 (Euler-Mascheroni constant)
Gray, Dodd, et al. "Thermo-optic multistability and relaxation in silicon microring resonators with lateral diodes." Physical Review Applied 14.2 (2020): 024073.

## Slide 28: Free-carrier Oscillations (FCO)
Realization of FC amplification with wave length above and around 2.0 µm
  Limit on Carrier Lifetime
  Upper bound on the effective loss that arises from screening the free-carrier sweepout field
    Generation rate
Hamerly, Ryan, et al. "Conditions for parametric and free-carrier oscillation in silicon ring cavities." Journal of Lightwave Technology 36.19 (2018): 4671-4677.
TPA:
Notes: anomalous dispersion
Dispersion that occurs when the medium's index of refraction decreases as the frequency of the propagating light increases. For a given medium, some wavelength ranges may produce anomalous dispersion while others produce normal dispersion.
In physics, screening is the damping of electric fields caused by the presence of mobile charge carriers. It is an important part of the behavior of charge-carrying fluids, such as ionized gases (classical plasmas), electrolytes, and charge carriers in electronic conductors (semiconductors, metals).

## Slide 29
Hamerly, Ryan, et al. "Conditions for parametric and free-carrier oscillation in silicon ring cavities." Journal of Lightwave Technology 36.19 (2018): 4671-4677.
f(ζ) = 1, V0 = −15 V, w = λ/1.55